## Slide 1: WebRTC multipoint conferencing
with recording using a Media Server

## Slide 2: Goal: WebRTC conferencing prototype that
allows more than four participants to communicate simultaneously
supports recording of conversations
allows participants in restrictive network environments to take part in conversations
optionally allows SIP-Clients (soft/hard phones), and Teleconferencing systems to connect to a conference

## Slide 3: WebRTC introduction
Peer-to-Peer based communication solution for all devices
Not dependent on OS, proprietary plugins or other programs
Most known for video chats between Google Chrome and Mozilla Firefox
Uses SDP to instantiate sessions
No signaling method is defined
Jointly defined by the W3C WebRTC Working Group (browser API) and the IETF RTCWEB Work Group (protocols)

## Slide 4: WebRTC triangle
Source: Iya Grigorik, 2013 High-performance browser networking

## Slide 5: Important bits – The API
RTCPeerConnection main object used by a web application in the browser
  Create connections between peers
  Handle SDP offers and answers
  ICE agent to find and negotiate usable IP addresses and port numbers (ICE candidates)
  Receive and send media streams
media stream requested using the MediaStream API
  Multiple video and audio tracks
RTCDataChannel TCP based, used to send arbitrary non-media data

## Slide 6: Device types
WebRTC device conforms to the protocol specifications
WebRTC browser WebRTC device that also supports the full ECMAScript API.
WebRTC gateway WebRTC device that mediates media traffic to non-WebRTC devices and may not conform to all protocol specifications.
UDP based protocols for the peer connection and TCP based ones for the data channel including encryption with TLS and DTLS
Connect PSTN telephone and WebRTC browser
Connect WebRTC browser to a multicast endpoint

## Slide 7: Goals: WebRTC conferencing prototype that
allows more than four participants to communicate simultaneously
supports recording of conversations
allows participants in restrictive network environments to take part in conversations
optionally allows SIP-Clients (soft/hard phones), and Teleconferencing systems to connect to a conference

## Slide 8: Multipoint conferencing
Source: Ilya Grigorik, 2013 High-performance browser networking

## Slide 9: Who records a conference
conference participant
- High processing power on client
- Distribution complicated
dedicated client
- Additional device needed
- Distribution complicated
- One more connection for every participant
Each participant records himself
Uploads recording to center
Recording with a centralized entity
Entity distributes streams to participants
Stores the streams

## Slide 10: Restrictive network environments
To establish a direct connection, a publicly accessible IP address is needed
ICE (Interactive Connectivity Establishment)
  STUN (Session Traversal Utilities for NAT) UDP, TCP, http, https
  TURN (Traversal using Relays around NAT)

## Slide 11: Restrictive network environments

## Slide 12: Connecting SIP devices
Session Instantiation Protocol
Text based protocol
Uses SDP to describe media streams (and their initialization parameters)
No mandatory codecs – transcoding is needed
PSTN telephone behaves the same as a teleconferencing solution with four cameras and microphones

## Slide 13: Media Server
Comparison of multipoint architectures

## Slide 14: Participant in a full mesh conference
4 Participants
Each participant
  3 uploads
  3 downloads
  3 Mbit/s bandwidth each up- and downstream for VGA video
7 participants:
Bandwidth of 12Mbit/s
WLAN 802.11b does not suffice

## Slide 15: Participant in a relayed conference
4 Participants
Each participant
  1 upload
  3 downloads
  4 Mbit/s bandwidth for VGA video
10 participants:
Bandwidth of 18.4Mbit/s
WLAN 802.11g needed

## Slide 16: Participant in a mixed conference
4 Participants
Each participant
  1 upload
  1 download
  2 Mbit/s bandwidth for VGA video
25 participants:
Bandwidth of 2 Mbit/s
Might work on 3G

## Slide 17: Media Server
Relayed conference
  2 participants: 4.1 Mbit/s needed
  4 participipants: 16.4 Mbit/s needed
  7 participants: 50.2 Mbit/s needed
  10 participants: 102.4 Mbit/s needed
Mixed conference
  2 participants: 4.1 Mbit/s needed
  4 participants: 8.2 Mbit/s needed
  7 participants: 14.3 Mbit/s needed
  10 participants: 20.5 Mbit/s needed
High strain on network device
High processing power needed

## Slide 18: Bandwidth recommendations (at 15fps)
Entry | Resolution | Recommended bandwidth | Minor hickups (1 freeze per minute) | Maximum used bandwidth
QCIF | 176x144 | 384kbit/s | 200kbit/s | 700kbit/s
CIF | 352x288 | 700kbit/s | 384kbit/s | 2000kbit/s
VGA | 640x480 | 1024kbit/s | 512kbit/s | 2100kbit/s
HD 720p | 1280x720 | 1900kbit/s | 1024kbit/s | 2500kbit/s
HD 1080p | 1920x1080 | - | - | -
One stream was tested on a virtual network device that was limited using the Network Emulator Toolkit

## Slide 19: Open Source Media Servers
Kurento http://www.kurento.org/ (LGPL)
Doubango https://code.google.com/p/telepresence/ (GPL)
Jitsi https://jitsi.org/Projects/JitsiVideobridge (MIT)
Licode http://lynckia.com/licode/ (MIT)
Kurento http://www.kurento.org/ (LGPL)

## Slide 20: Architecture

## Slide 21: Example: Start a conversation

## Slide 23: Goals
Most of the goals for this thesis were achieved with the simucos prototype:
Conferences can be recorded on the media server as VP8 or h.264 video files.
Many clients may participate in a conference, the highest number tested was 25 in a mixed conference, and 14 in a relayed conference.
Participants in restrictive network environments can connect to a conference using a STUN or TURN server.
Only the optional goal to add support for SIP clients into simucos was not implemented due to the chosen Node.js architecture.

## Slide 24: Conclusion and prospect
WebRTC is a mature technology
WebRTC has disruptive qualities:
  Solutions are achievable that would need more experience, more man-power and more time with other communication solutions

## Slide 25: Future ideas
Switching a peer-to-peer conference to a media server
Hybrid architecture approach
  Lessen strain on media server by using peer-to-peer meshes
Dynamic architecture approach
  Develop algorithms to optimize the hybrid architecture approach
Peer-to-peer broadcasting of one presenter
  Tree based structure
  Ring structure

## Slide 26: Bright future for WebRTC
New features in WebRTC 1.0
  Unified statistics API
  Promises instead of callbacks
Object RTC (ORTC)
  Effort to create the next version of WebRTC (backed by Microsoft and Google)
  Exchange text-based SDP with a JS object model
  Developers gain access to lower-level functions (e.g. Codec settings per track)
  More powerful and flexible JavaScript API

## Slide 27: www.mikogo.com Questions?
Thesis available at:
https://github.com/marc136/thesis
Email: mwalter@mikogo.com

## Slide 28: More Time?
Some other stuff...
Image sources
Title page:
  Top left: http://lifestyle.beiruting.com/wp-content/uploads/2011/09/business-man-resume.jpg
  Top center: http://www.jenningswire.com//wp-content/uploads/2014/01/Businessman1.jpg
  Top right: http://bizblog.cosmobc.com/files/2015/03/Business-Man.jpg
  Bottom left: http://ak3.picdn.net/shutterstock/videos/4885424/preview/stock-footage-businessman-enjoying-book-on-digital-ebook-reader-device-on-train-journey.jpg
  Bottom center: http://www.careerealism.com/wp-content/uploads/2011/11/Mature-Businessman-Thinking.jpg
  Bottom right: http://thumbs.dreamstime.com/z/picture-confused-woman-smartphone-bright-32589001.jpg
28: http://www.kurento.org/docs/current/introducing_kurento.html

## Slide 29: Kurento Media Server
Sample media pipeline

## Slide 30: Network Emulation Toolkit (NEWT)
http://blogs.msdn.com/b/lkruger/archive/2009/06/08/introducing-true-network-emulation-in-visual-studio-2010.aspx
https://blog.mrpol.nl/2010/01/14/network-emulator-toolkit/
Limit bandwidth
Simulate high traffic
Simulate packet loss

## Slide 31: ICE Candidate Gathering

## Slide 32: Symmetric NAT